## Slide 1
NODEMCU and BLYNK APP
LECTURE 8:
TAPIT
INTERNET OF THINGS

## Slide 2
TAPIT
PIN OUT

## Slide 3
TAPIT
Blynk is a Platform with iOS and Android apps to control nodeMCU, and the likes over the Internet.
Blynk was designed for the Internet of Things.
BLYNK
Its features:
Supports majority of development boards like Arduino, esp8266
Easy to use
Awesome widgets like LCD, push buttons, labelled value, graphs
Not restricted to local Wifi network
Direct pin manipulation with no code writing
Easy to integrate and add new functionality using virtual pins

## Slide 4
TAPIT
How does BLYNK work?
Now imagine: every time you press a Button in the Blynk app, the message travels to space the Blynk Cloud, where it magically finds its way to your hardware. It works the same in the opposite direction and everything happens in a blynk of an eye.
Notes: There are three major components in the platform:
Blynk App - allows to you create amazing interfaces for your projects using various widgets we provide.
Blynk Server - responsible for all the communications between the smartphone and hardware. You can use our Blynk Cloud or run your private Blynk server locally. It’s open-source, could easily handle thousands of devices and can even be launched on a Raspberry Pi.
Blynk Libraries - for all the popular hardware platforms - enable communication with the server and process all the incoming and outcoming commands.

## Slide 5
There are three major components in the platform:
Blynk App - allows to you create amazing interfaces for your projects using various widgets we provide.
Blynk Server - responsible for all the communications between the smartphone and hardware. You can use our Blynk Cloud or run your private Blynk server locally. It’s open-source, could easily handle thousands of devices and can even be launched on a Raspberry Pi.
Blynk Libraries - for all the popular hardware platforms - enable communication with the server and process all the incoming and outcoming commands.
TAPIT

## Slide 6
“Ok, I want it. What do I need to get started?”
1. Hardware.
Blynk supports more than 400 boards already, including support for Arduino, Particle, ARM mbed, TI Energia, MicroPython, Node.js, OpenWRT and many Single Board Computers. Blynk works over the Internet. This means that the hardware you choose should be able to connect to the internet. Some of the boards will need an Ethernet or Wi-Fi Shield to communicate, others are already Internet-enabled.

## Slide 8
2. A Smartphone
“Ok, I want it. What do I need to get started?”
The Blynk App is a well designed interface builder. It works on both iOS and Android.

## Slide 9
3. Blynk Library

## Slide 10
Button
Works in push or switch modes. Allows to send 0/1 (LOW/HIGH) values. Button sends 1 (HIGH) on press and sends 0 (LOW) on release.
Slider
Similar to potentiometer. Allows to send values between MIN and MAX.
Timer
Timer triggers actions at a specific time. Even if smartphone is offline. Start time sends 1 (HIGH). Stop time sends 0 (LOW).
Joystick
Control servo movements in 4 directions
Controllers

## Slide 11
Displays
Value Display
Displays incoming data from your sensors or Virtual Pins.
LED
A simple LED for indication. You need to send 0 in order to turn LED off. And 255 in order to turn LED on. Or just use Blynk API as described below :
Gauge
A great visual way to display incoming numeric values.
LCD
This is a regular 16x2 LCD display made in our secret facility in China

## Slide 12
SuperChart
SuperChart is used to visualise live and historical data. You can use it for sensor data, for binary event logging and more.
Terminal
Displays data from your hardware. Allows to send any string to your hardware.
Video Streaming
Simple widget that allows you to display any live stream. Widget supports RTSP (RP, SDP), HTTP/S progressive streaming, HTTP/S live streaming.
Level Display
Displays incoming data from your sensors or Virtual Pins.

## Slide 13
Notifications
Twitter
Twitter widget connects your Twitter account to Blynk and allows you to send Tweets from your hardware.
Email
Email widget allows you to send email from your hardware to any address.
Push Notifications
Push Notification widget allows you to send push notification from your hardware to your device.

## Slide 14
RTC
Real-time clock allows you to get time from server. You can preselect any timezone on UI to get time on hardware in required locale. No pin required for RTC widget.
Music Player
Simple UI element with 3 buttons - simulates music player interface.

## Slide 16
TAPIT

## Slide 17
TAPIT

## Slide 18
TAPIT

## Slide 19
TAPIT

## Slide 20
TAPIT

## Slide 21
TAPIT
Blynk Library Arduino IDE:
Sketch -> Include Library -> Manage Libraries, Search Blynk then install.

## Slide 22
TAPIT

## Slide 23
TAPIT
Notes: http://docs.blynk.cc/